## Slide 1: Working with ros bag

## Slide 2: Working with ros bags
Bags (.bag files) are files used in ROS for logging, analyzing, visualizing and data playback
Bags are created by the rosbag package, which subscribe to a topic and record the serialized data.
Bags can also play the data received either to the same topic or to a different one.

## Slide 3: Working with ros bags
The rosbag command-line tool provides functionality for ROS bags.
We will first take a look at the basic commands:
  record: record the contents of topic(s) into a bag file.
  info: summarize the content of a bag file
  play: playback the content of one or more bag file

## Slide 4: Rosbag record
In this section, we will look at how to use the record command
The rosbag record command subscribes to a topic and log the serialized ROS messages into a single bag file
The file is written as the messages are sent over the wire
We will look at specific commands and how they work

## Slide 5: Rosbag record
$ rosbag record –h: open help menu
$ rosbag record –a: record all topics currently being used
  The bag file will be put in your current directory
$ rosbag record <topic_1> <topic_2> … : records the messages sent over specified topics.
$ rosbag record –O NAME: record to a bag file with the name NAME.bag
$ rosbag record –o PREFIX: prepend PREFIX to the beginning of the bag name
  When a file name is not declared, the .bag file with have the time of record as its name
$ rosbag record –p: publish and message to the topic “begin_write” when the record being to write a new bag (melodic only)

## Slide 6: Rosbag info
rosbag info displays a human-readable summary of the contents of the bag file
  The summary contains: start and end time, topics and their types, message counts, frequency, …
rosbag info –h: show the help menu
rosbag info <bag_file>: display a summary of the content of the bag file

## Slide 7: Rosbag play
Rosbag play reads the content of one or more bag file and plays them back in a time-synchronized fashion
If multiple bags are played, the delay between the recording time of them will be portrayed as well
  For example, if your record the first bag file, wait an hour then record the second one, when both files are played back, the first file will play, then an hour delay, then then second file will play.
The replay process can be paused with the spacebar at anytime

## Slide 8: Rosbag play
rosbag play –h: show the help menu
rosbag play <bag_files>: play (publish) the contents of a given bag
rosbag play -i: play all messages without waiting
  This is a way to workaround the delay with the timing
rosbag play –s SEC: start SEC seconds into the bag
rosbag play –r FACTOR: playback with the FACTOR times the rate
rosbag play –l: loop the playback untils interrupt