## Slide 1: Introduction to ROS

## Slide 2: What is ROS?
Robot Operating System (ROS) is a flexible framework, providing various tools and libraries to write robotic software.
ROS was first started in 2007 is growing very fast, being used more and more frequently worldwide, even in high-end robotic companies.

## Slide 3: Good things about ros?
High-end capabilities
Tons of tools
Support for high-end sensors and actuators
Inter-platform operability
Modularity
Concurrent resource handling
Active community

## Slide 4: Difficulties approaching ros
Difficulty in learning
Difficulties in starting with simulation
Difficulties in robot modeling
Potential limitations (lack of real-time application development support/complexity to implement robust multi-robot distributed application)
Ros is a commercial robot product

## Slide 5: Ros filesystem level
ROS can be referred to as a meta-operating system
Similar to a real OS, ROS files are organized on the hard disk in a manner as described in the figure
Each block of the figure will be briefly explained in the next pages

## Slide 6: ROS filesystem level (cont.)
Package: the most basic unit of ROS software, contains processes called node
Package manifest(.xml file): a file inside a package, containing information about the package.
Metapackage: one or more packaged loosely grouped together to form a logical package.
Metapackage manifest(.xml file): similar to normal package manifest but declare and <export> tag

## Slide 7: Ros filesystem level (cont.)
Messages(.msg): The type of information used by processes to communicate with each other
Service(.srv): a type of request/reply interaction between processes
Repositories: Most of ROS are maintained using a Version Control System (VCS). Repository is a collection of files that share a common VCS

## Slide 8: ROS package
This part will go into details about ROS packages
A typical ROS package will have a structure as described in the figure
Each block represent a folder commonly found in a ROS package
CMakeList.txt: a file contains directive on how to compile the package
Package.xml: package manifest file. Unique to this package

## Slide 9: ROS package
Config: contains configuration files
Include: contains header/libraries
Script: contains Python scripts
Src: contains C++ code
Launch: contains .launch files that are used to run multiple nodes at once
Msg: contains .msg files
Srv: contains .srv files
Action: contains .action files

## Slide 10: Ros computation graph level
The computation in ROS is done using a network of a process called ROS nodes.
This computation network is called computation graph

## Slide 11: Main concepts in Ros computation graph
Nodes: the process that performs the computation, written using ROS client libraries. Each node is a simple functionality/process that contributes to the final work
Master: provides the name registration and look up for all other nodes.
Parameter server: part of the master that allows data to be stored in a central location. All nodes can access and modify this
Messages: nodes communicate with each other using messages, which are data structures. These messages are stored in .msg files
Topics: messages are transported through named bus called topics.
Service: in some cases, the communication through simple messages is not enough. Service (stored in .srv files) is a fast request/respond type of interaction
Logging: In case we need to store data, ROS provides a logging system through Bagfiles

## Slide 12: Ros nodes
ROS nodes are processes that perform computation using ROS client libraries (roscpp, rospy, etc)
Nodes communicate with each other using ROS Topic, Services and Parameters.
A package can contain many nodes, each handles a computation/functionality
Each node has a unique name that identifies themselves and their function in the system

## Slide 13: Ros messages
ROS messages is how nodes communicate with each other
ROS messages are a simple data structure containing field types (primitive datatypes and arrays of primitive datatypes)
Communication using ROS message is unidirectional
The node sending the message is called publisher
The node receiving the message is called subscriber
ROS messages are stored in .msg files, which are gathered in the msg folder of a ROS package
The following is an example of the content of a .msg file
*Note: Header is a special type in ROS, contains a timestamp and coordinate frame information that are commonly used in ROS

## Slide 14: rOS topics
ROS topics are named buses in which ROS messages are exchanged
The pub/sub is decoupled, meaning there can be many publisher and subscriber to the same topic.
The subscriber only receive message of matching type to the one published

## Slide 15: Ros services
ROS service is a type of ROS message
ROS service contains a request field and a respond field, separated by a “---”, each is similar in format to a ROS message
ROS service is bidirectional communication (request/respond)
The node that sends the request and wait for the respond is called client
The node that handles the request and send back the respond is call service
ROS services are stored in .srv files, which are gathered in the srv folder of the ROS package
The following is an example of the content of a .srv file

## Slide 16: Ros bags
ROS bags (.bag files) are used for storing message data from topics and services
The ROS bag can subscribe to one or more topics and store the message’s data in a file as it’s received
Bags are mainly used for data logging

## Slide 17: RoS master
The ROS master central point, associating unique names and IDs to ROS elements active in our system.
When a new node is created, it will register its details in the master
When a node publish a topic, it will give the topic details to the master
The master will check for subscriber(s) of a topic and share the info of the publisher to them
Once the pub/sub are connected, the master has no role in the communication between them

## Slide 18: Working with ROS
Most of ROS functionalities are accessed through command lines.
This part will cover some commonly used/helpful commands when using ROS
*Note: this part requires a full installation of ROS. Please install ROS and setup the workspace according to the provided tutorial.

## Slide 19: Working with ROS (package)
catkin_create_pkg <package_name> <depend1> <depend2> …: Create a new package at the current directory
catkin_make: build the whole package in the workspace
rospack: get information about the ROS package
rosdep: install all dependency for the package
roscd: change directory using a package name (work similar to regular cd)
roscp: copy a file from a package
rosed: edit a file (default editor is vim, can be changed)
rosrun: run an executable inside a package

## Slide 20: Working with ros (master)
roscore: starts the ROS master, ROS parameter server and rosout loggin node.
This command is needed before running any of the ROS nodes

## Slide 21: Working with ros (node)
rosnode info <node_name>: get information about the node
rosnode kill <node_name>: kill the running node
rosnode list: list all nodes
rosnode machine <machine_name>: list the nodes running on a particular machine
rosnode ping: check connectivity to a node
rosnode cleanup: purge the registration of unreachable nodes

## Slide 22: Working with ros (messages)
rosmsg show <message>: show the message description
rosmsg list: list all messages
rosmsg md5: displays md5sum of a message (checksum to confirm the pub/sub are exchanging the same data type)
rosmsg package: list the messages in a package
rosmsg packages <package_1> <package_2>: list the packages that contain messages

## Slide 23: Working with ros (topics)
rostopic bw /topic: displays the bandwidth used by a topic
rostopic echo /topic: print the content of a given topic in human readable format
rostopic find /message_type; find topics using the given message type
rostopic hz /topic: display the publishing rate of the topic
rostopic info /topic: print the information about an active topic
rostopic list: list all active topics
rostopic pub /topic message_type args: publish a value to a topic with the message type
rostopic type /topic: display the message type of the given topic

## Slide 24: Working with ros (service)
ROS service has 2 related command: rossrv and rosservice.
rossrv is used to provide information related to ROS service definition (.srv files). This command is similar to that of rosmsg and will not be covered again.
The rosservice usage will be covered in the next page

## Slide 25: Working with ros (service)
rosservice call /service args: call the service using the given argument
rosservice find service_type: find services in the given service type
rosservice info /services: print information about the given service
rosservice list: list the active services running on the system
rosservice type /service: print the service type of a given service

## Slide 26: Working with ROS (bags)
rosbag record <topic_1> <topic_2> -o <bag_name>: record the given topics into a bag file with the given name
rosbag play <bag_name>: playback the existing bag file

## Slide 27: Working with ros (parameter)
rosparam list: list all existing parameter
rosparam set <param_name> <value>: set a value in a given parameter
rosparam get <param_name>: retrieve a value from a given parameter
rosparam load <.yaml_file>: load parameter to the server from a .yaml file
rosparam dump <.yaml file>: dump the existing parameter into a .yaml file
rosparam delete <parameter_name>: delete the given parameter